## Slide 1
EduSound
Metrics
Listening to classrooms, not to people.
Proof-of-concept demonstration · May 2026

## Slide 2
Why classroom noise matters
Sound shapes attention, well-being and learning — silently.
55 dB
Threshold above which comprehension drops
60 %
of teachers report voice strain at work
2×
louder rooms hit students with hearing aids hardest

## Slide 3
What EduSound Metrics does
One simple loop, repeated all day, every day.
MEASURE
01
Six tiny mics per room, every few seconds.
SHOW
02
An LED in the room, a dashboard on any device.
COMPARE
03
Across rooms, across days, across the year.
DECIDE
04
Evidence for teachers and school leadership.

## Slide 4
Two architectures, one choice
One central mic vs. a swarm of tiny ones.
A
One central mic
+ Simple install
+ One viewpoint of the room
− Single point of failure
− Skewed by closest table
CHOSEN
B
Six distributed mini-mics
+ Real spatial coverage
+ Median filters out one loud table
- Lower dynamic sensitivity range.
- Highly complex installation and prone to failure.

## Slide 5
How it works
From the ceiling of the classroom to a phone anywhere in the world.
Mics
ESP32-S3
MQTT
broker.hivemq.com
Backend
Node.js + SQLite
Dashboard
Next.js
Public URL
Cloudflare Tunnel
No school IT changes
No open ports
Works from any phone

## Slide 6
The listening node
Each node = step-down PCB (fuse + TSR) + soldered USB-C pigtail + M5Stack ATOM Echo S3R.
Five complete listening nodes — each ATOM Echo wired to its own step-down PCB through a soldered pigtail.
2 comp.
soldered on the PCB (fuse + TSR 1-2450)
6
nodes per classroom (mesh)
1 bus
single 24 V line per room

## Slide 7
From sketch to circuit
Three steps from a pencil drawing to a board on the ceiling.
01
Sketch
Pencil on graph paper — first attempt at the perfboard layout.
02
Review
First digital pass with an Adafruit USB-C breakout — CC pull-ups spotted as wrong. Discarded.
03
Diagram
Corrected as-built schematic on 19×31 perfboard — only a 1 A fuse and a Traco TSR 1-2450, all soldered.
04
Build
Real board from IMG_144 — fuse + TSR soldered, 24 V wires up, USB-C pigtail down.

## Slide 8
From wall socket to ceiling mic
A repeatable wiring scheme — every classroom is identical.
24 V
supply
5 V
per node
USB-C
to ATOM Echo

## Slide 9
Built and installed
Custom step-down PCB, single 24 V bus, mounted on the ceiling.
Per-node PCB (close-up).
Mounted on the ceiling.
Ceiling junction box with 24 V terminal block.

## Slide 10
The room speaks for itself
Each mic glows. The class regulates the class.
< 50 dB
CALM
50–70 dB
WORKING
> 70 dB
TOO LOUD
No teacher voice required.

## Slide 11
Live view
One classroom, five active mics, real time.
44.7 dB
Room average
5 / 5
Active mics
<1 s
Update latency

## Slide 12
History — by lesson, by day
Slots align with the school timetable.
14 d
raw 5-s samples
6 mo
per-minute rollup
∞
per-hour rollup

## Slide 13
Awareness, not authority
The LED becomes the impartial referee.
“The class regulates the class.”
From “who is shouting?” to “what does our room sound like right now?”
Agree a target
Class & teacher set a dB goal for each activity.
Reflect together
End of lesson, the curve becomes a conversation.
De-escalate
The LED, not the teacher, says “too loud”.

## Slide 14
From data to decisions
Objective measurements replace opinions.
01
Spot problem rooms
Find rooms that are loud regardless of who occupies them.
02
Test interventions
Measure before & after acoustic panels, carpets, blinds.
03
Reshape the timetable
Identify the loudest slots — sometimes it's scheduling, not behavior.
04
Catch anomalies early
A sudden baseline shift often signals a broken HVAC unit.

## Slide 15
Their data, their questions
Data literacy with a dataset students actually care about.
?
When is our room loudest — and why?
?
Do Fridays sound different from Mondays?
?
Did the new seating plan really change anything?
?
Is the room next door noisier than ours?
Every chart is also a JSON endpoint — export to Excel, Sheets, Python, R or Scratch.

## Slide 16
Privacy by design
Measure the room, not the people in it.
YES
✓ dB level (every few seconds)
✓ min / max / avg per minute
✓ Anonymous room label
NEVER
✗ Audio recording
✗ Speech / transcription
✗ Names, faces, identifiers
✗ Location data

## Slide 17
What the data is already telling us
21 days of continuous monitoring in one classroom — 7 microphones, 24/7.
21 days
of continuous recording, no dropouts
42k samples
captured in one school day, 7 mics
14.6 dB
instantaneous spread across mics in the same room — the distributed model earns its keep
47 dB
loudest lesson average (5th period, just after lunch)
25 dB
quietest moment of the day — the break, when the room is empty
0 %
of the day above 70 dB — the room never tipped into red

## Slide 18
What this PoC has shown
Stable
weeks of continuous monitoring
Off-the-shelf
ESP32 + open software is enough
Behavioral
the LED changes the room
Year-long
rollups keep history meaningful
Versatile
teach, regulate, manage
Open
MIT-licensed, replicable
EduSound Metrics · Thank you